### Initialization for 8257 DMA

- DMA Address Registers		– Start Point of Data Transfer

- Terminal Count Registers	– Length of transfer (N - 1)  & Access Type

- Mode Set Register 		– Modes

### The Terminal Count Register

| Bit 15 | Bit 14 | Bit 13 ~ Bit 0 | Function |
| --- | --- | --- | --- |
| 0 | 0 | Number of bytes MINUS 1 | Verify |
| 0 | 1 |  | Write |
| 1 | 0 |  | Read |
| 1 | 1 |  | Illegal |

### Mode Set Register

|  | Register Byte I/O Addr.Offset CH-0 DMA Address LSB +0 MSB +0 CH-0 Terminal Count LSB +1 MSB +1 … … … CH-3 DMA Address LSB +6 MSB +6 CH-3 Terminal Count LSB +7 MSB +7 Mode Set Register 8-bit +8 Status Register 8-bit +8 |
| --- | --- |

# Text boxes

Auto-load

TC-STOP

Extended-Write

Rotating Priority

Enable Chn. 0

Enable Chn. 1

Enable Chn. 2

Enable Chn. 3

7

6

5

4

3

2

1

0

CH3

CH2

CH1

CH0